## Slide 1: National Water Policy of Bangladesh
Course: GEST-5102

## Slide 2: Introduction
Water is one of the most vital natural resources for Bangladesh — a country crisscrossed by hundreds of rivers and heavily dependent on agriculture and fisheries. However, increasing population, pollution, climate change, and transboundary water issues have made water management a major challenge. To address these challenges, the Government of Bangladesh adopted the National Water Policy (NWP) in 1999 — a landmark framework for the management, development, and equitable distribution of the country's water resources.

## Slide 3: Objectives of the National Water Policy
a. To address issues related to development of all forms of surface water and ground water and management of these resources in an efficient and equitable manner
b. To ensure the availability of water to all elements of the society including the poor and the underprivileged, and to take into account the particular needs of women and children
c. To accelerate the development of sustainable public and private water delivery systems with appropriate legal and financial measures and incentives, including delineation of water rights and water pricing

## Slide 4: Conti…………..
d. To bring institutional changes that will help decentralize the management of water resources and enhance the role of women in water management
e. To develop a legal and regulatory environment that will help the process of decentralization, sound environmental management, and improve the investment climate for the private sector in water development and management
f. To develop a state of knowledge and capability that will enable the country to design future water resources management plans by itself with economic efficiency, gender equity, social justice and environmental awareness to facilitate achievement of the water management objectives through broad public participation

## Slide 5: River Basin Management
a. Work with co-riparian countries to establish a system for exchange of information and data
b. Work with co-riparian countries for a joint assessment of all the international rivers
c. Work jointly with co-riparian countries to share the water resources
d. Make concerted efforts, in collaboration with co-riparian countries, for watershed preservation and reduction of land degradation
e. Work jointly with co-riparian countries for the prevention of chemical and biological pollution
f. Seek international and regional cooperation for education, training, and research in basin management

## Slide 6: Water Rights and Allocation
a. The government will exercise its water allocation power in identified scarcity zones on the basis of specified priorities
b. For sustaining rechargeable shallow groundwater aquifers, the Government will regulate the extraction of water in the identified scarcity zones with full public knowledge
c. Specific drought monitoring and contingency plans will be prepared for each region experiencing recurrent seasonal shortages of water
d. The Government may empower the local government to exercise its right to allocate water in scarcity zones
e. The Government may confer water rights on private and community bodies.
f. In specifying surface water rights, the minimum requirement of stream-flow for maintaining the conveyance channel will be ensured

## Slide 7: Water Supply and Sanitation
a. Facilitate availability of safe and affordable drinking water supplies through various means, including rainwater harvesting and conservation.
b. Preserve natural depressions and water bodies in major urban areas for recharge of underground aquifers and rainwater management.
c. Mandate relevant public water and sewerage institutions to provide necessary drainage and sanitation, including treatment of domestic wastewater and sewage and replacement of open drains and construction of sewers, in the interest of public health.
d. Empower, and hold responsible, municipalities and urban water and sewerage institutions to regulate the use of water for preventing wastage and pollution by human action.
e. Mandate local governments to create awareness among the people in checking water pollution and wastage.
Promotes monitoring and regulation of water quality by the DoE.

## Slide 8: Water and Agriculture
a. Encourage and promote continued development of minor irrigation, where feasible, without affecting drinking water supplies
b. Encourage future groundwater development for irrigation by both the public and the private sectors, subject to regulations that may be prescribed by Government from time to time.
c. Improve efficiency of resource utilisation through conjunctive use of all forms of surface water and groundwater for irrigation and urban water supply.
d. Strengthen crop diversification programmes for efficient water utilisation.
e. Strengthen the regulatory system for agricultural chemicals that pollute ground and surface water, and develop control mechanism for reducing non-point pollution from agro-chemicals.
f. Strengthen appropriate monitoring organisations for tracking groundwater recharge, surface and groundwater use, and changes in surface and groundwater quality

## Slide 9: Water and Industry
a. Zoning regulations will be established for location of new industries in consideration of fresh and safe water availability and effluent discharge possibilities.
b. Effluent disposal will be monitored by relevant Government agencies to prevent water pollution.
c. Standards of effluent disposal into common watercourses will be set by WARPO in consultation with DOE.
d. Industrial polluters will be required under law to pay for the cleanup of water- body polluted by them

## Slide 10: Water for Fisheries and Wildlife
a. Fisheries and wildlife will receive due emphasis in water resource planning in areas where their social impact is high.
b. Measures will be taken to minimize disruption to the natural aquatic environment in streams and water channels.
c. Drainage schemes, will avoid state-owned swamps and marshes that have primary value for waterfowl or other wildlife.
d. Water bodies like baors, haors, beels, roadside borrow pits, etc. will, as far as possible, be reserved for fish production and development.
e. Water development plans will not interrupt fish movement and will make adequate provisions in control structures for allowing fish migration and breeding.
f. Brackish aquaculture will be confined to specific zones designated by the Government for this purpose.

## Slide 11: Water and Navigation
a. Water development projects should cause minimal disruption to navigation and, where necessary, adequate mitigation measures should be taken.
b. Minimum stream-flows in designated rivers and streams will be maintained for navigation after diversion of water for drinking and municipal purposes.
c. Dredging and other suitable measures would be undertaken, wherever needed, to maintain navigational capability of designated waterways.

## Slide 12: Water for Hydropower and Recreation
a. Mini-hydropower development schemes may be undertaken provided they are economically viable and environmentally safe.
b. Recreational activities at or around water bodies will be allowed provided it is not damaging to the environment.

## Slide 13: Water and flood management
Emphasizes non-structural measures like floodplain zoning and community-based disaster management.
Promotes early warning systems and flood-proofing strategies.
Reduces reliance on embankments and large-scale engineering alone.

## Slide 14: Water for the Environment
a. Give full consideration to environmental protection, restoration and enhancement measures consistent with the National Environmental Management Action Plan (NEMAP) and the National Water Management Plan (NWMP)
b. Adhere to a formal environmental impact assessment (EIA) process, as set out in EIA guidelines and manuals for water sector projects, in each water resources development project or rehabilitation programme of size and scope specified by the Government from time to time
c. Ensure adequate upland flow in water channels to preserve the coastal estuary eco-system threatened by intrusion of salinity from the sea
d. Protect against degradation and resuscitate natural water-bodies such as lakes, ponds, beels, khals, tanks, etc. affected by man-made interventions or other causes
e. Completely stop the filling of publicly-owned water bodies and depressions in urban areas for preservation of the natural aquifers and environment
f. Take necessary steps to remove all existing unauthorized encroachments on rivers and watercourses
g. Stop unplanned construction on riverbanks
h. Encourage massive afforestation and tree coverage specifically in areas with declining water table
i. Enforce the "polluter pay" principle in the development of regulatory guidelines for all regulatory actions designed to protect public health and the environment

## Slide 15: Preservation of Haors, Baors, and Beels
a. Natural water bodies such as beels, haors, and baors will be preserved for maintaining the aquatic environment and facilitating drainage.
b. Only those water related projects will be taken up for execution that will not interfere with the aquatic characteristics of those water bodies.
c. Haors that naturally dry up during the winter will be developed for dry season agriculture.
d. Take up integrated projects in those water bodies for increasing fish production.
e. Natural water bodies will be developed, where possible, for recreational use in support of tourism

## Slide 16: Institutional Framework
Ministry of Water Resources (MoWR) – main policymaking body.
Water Resources Planning Organization (WARPO) – responsible for planning and coordination.
Bangladesh Water Development Board (BWDB) – implements flood control, irrigation, and drainage projects.
Local Government Institutions (LGIs) – engage in small-scale water resource management and maintenance.

## Slide 17: Future directions and updates
The policy calls for periodic review and updating to reflect new realities.
Integration with the Bangladesh Delta Plan 2100 (BDP 2100).
Promotion of climate-resilient water infrastructure.
Digitalization of water data and mapping for better planning.

## Slide 18: Conclusion
The National Water Policy of 1999 remains a cornerstone of water governance in Bangladesh. It provides a comprehensive framework for managing water resources in a way that is sustainable, participatory, and environmentally sound. However, its effectiveness depends on institutional coordination, technological innovation, and public awareness to ensure that every citizen of Bangladesh can benefit from safe, reliable, and sustainable water resources.

## Slide 19
Thanks